## Slide 1: Physical Security
CIS 360 – Prof. C. R. Johnson
University of Wisconsin – Stevens Point

## Slide 2: Physical Security Systems
The original security question – how to keep people you down want in from getting in, and how to keep things you don’t want getting out from getting out.
This simple question has grown increasingly complicated as technology evolves and provides new weaknesses to systems.
At the core of physical security is still the same issue, but now with many more considerations.

## Slide 3: Definition
Physical security is the protection of personnel, hardware, programs, networks, and data from physical circumstances and events that could cause serious losses or damage to an enterprise, agency, or institution. This includes protection from fire, theft, vandalism, natural disasters, and terrorism.

## Slide 4: Attack Vectors into Control Systems

## Slide 5: A Control System
Sensor(s) +
Actuator(s) +
Controller(s)

## Slide 6: Types of Industrial Control Systems (ICS)
Supervisory Control And Data Acquisition (SCADA)
Automation
Process Control Systems (PCS)
Distributed Control Systems (DCS)
Notes: Supervisory Control and Data Acquisition (SCADA)
  Large distances, supervisory control, non-real-time (minutes)
  Used in power (transmission and distribution), gas, oil, water, wastewater, rail, etc.
Process Control Systems (PCS)
  Closed loop, central control, near real-time (seconds)
  Used in refining, chemical, food, pharmaceutical, etc.
Distributed Control Systems (DCS)
  Similar to PCS but multiple controllers physically close to processes
  Used in generation, manufacturing, refining, chemical, food, pharmaceutical, etc.
Automation aka Discrete Control
  Similar to DCS, real-time (milliseconds)

## Slide 7: Historical ICS
Proprietary
Complete vertical solutions
Customized
Specialized communications
  Wired, fiber, microwave, dialup, serial, etc.
  100s of different protocols
  Slow; e.g. 1200 baud
Long service lifetimes: 15–20 years
Not designed with security in mind
Notes: the slogan “tomorrow’s technology today” of high-tech industries is turned around in the control systems world to “yesterday’s technology tomorrow”.
“security” in power usually means reliability of the grid
there is a big difference between “robust to accidental events” and “robust to intentional engineered attacks”

## Slide 8: Modern ICS Trends
Third Party
Controllers,
Servers, etc.
Serial, OPC
or Fieldbus
Engineering
Workplace
Device Network
Firewall
Services
Network
Third Party Application Server
Application
Server
Historian
Server
Workplaces
Enterprise
Optimization Suite
Mobile Operator
Connectivity
Server
Control
Network
Redundant
Enterprise Network
Serial
RS485
IP
Internet
Enterprise Network
Notes: at the bottom, IEDs are usually connected to sensors and controllers by automation networks such as HART, Fieldbus, Profibus, or increasingly by Ethernet
although one process control vendor already offering IPV6 wireless on battery-powered sensors
next level of network consists of ICS master and systems used for operating and managing the ICS
next level of network provides advanced applications, such as optimization and gateways to the enterprise network
Adoption of COTS (Commercial-Off-The-Shelf) technologies
  Operating systems—Windows, WinCE, various embedded RTOSes
  Applications—Databases, web servers, web browsers, etc.
  IT protocols—HTTP, SMTP, FTP, DCOM, XML, SNMP, etc.
  COTS software and systems have more capabilities and are cheaper than proprietary systems, and do not leave vendors stranded on out-of-date technology
Connectivity of ICS to enterprise LAN
  Improved business visibility, business process efficiency: eg. supply chain management, production scheduling, order tracking, and fault monitoring
  (optimize part and supply sourcing, schedule production to better meet business requirements and avoid contract penalties)
  Remote access to control center and field devices: eg. remote diagnosis and repair, reduction of personnel at remote sites
Adoption of IP Networking
  Common in higher level networks, gaining in lower levels
  Many legacy protocols wrapped in TCP or UDP
  Most new industrial devices have Ethernet ports
  IP penetrating into lower levels of ICS networks due to greater performance, lower cost, more capabilities than proprietary networks
    Ease of connectivity to other systems
    Greater performance
    Lower cost
    Interoperability
    Future proofing
rate at which these trends are progressing varies between ICS and process control and between control center, communications, and field devices

## Slide 9: Technology Trends in ICS
COTS (Commercial-Off-The-Shelf) technologies
  Operating systems—Windows, WinCE, embedded RTOSes
  Applications—Databases, web servers, web browsers, etc.
  IT protocols—HTTP, SMTP, FTP, DCOM, XML, SNMP, etc.
  Networking equipment—switches, routers, firewalls, etc.
Connectivity of ICS to enterprise LAN
  Improved business visibility, business process efficiency
  Remote access to control center and field devices
IP Networking
  Common in higher level networks, gaining in lower levels
  Many legacy protocols wrapped in TCP or UDP
  Most new industrial devices have Ethernet ports
  Most new ICS architectures are IP-based
Notes: trends relevant to networking and security
rate at which these trends are progressing varies between ICS and process control and between control center, communications, and field devices
connectivity improves business efficiency by better supply chain management, just-in-time production, order tracking, fault monitoring, etc. in addition to direct optimization of process itself
IP networking:
  Ease of connectivity to other systems
  Greater performance
  Lower cost
  Interoperability
  Future proofing

## Slide 10: Physical Control security is terrible
Most control systems emphasize stability over all, and often have less development resources.
  Remaining on outdated OS
  Going unpatched
  Requiring network access to work
  Have separate user repositories / access controls

## Slide 12: With Physical Access
Firewall rules are bypassed
Hardware can be manipulated
Security can be broken
Physical destruction is possible
Hardware hacking is a thing
Plus theft, increasing the amount of time an attacker has to work.

## Slide 13: Layered Security
Physical Barriers
    Fences
    Alarms
    Restricted Access Technology
Physical Restrictions
    Air Gapping
    Removable Media
    Remote Storage
Personnel Security Practices
    Limited Access
    Training
    Consequences/Deterrence

## Slide 14: Physical Barriers
Hardened Facilities
    Fences
    Guards
    Alarms
    Locks
    Restricted Access Technologies
      Biometrics
      Coded Entry
      Badging
    Signal Blocking (Faraday Cages)

## Slide 15: Outer Protective Layers
Structure
  Fencing, gates, other barriers
Environment
  Lighting, signs, alarms
Purpose
  Define property line and discourage trespassing
  Provide distance from threats

## Slide 16: Unpatched Systems
Many ICS systems are not patched current
  Particularly Windows servers
  No patches available for older versions of windows
OS and application patches can break ICS
  OS patches are tested for enterprise apps
Uncertified patches can invalidate warranty
Patching often requires system reboot
Before installation of a patch:
  Vendor certification—typically one week
  Lab testing by operator
  Staged deployment on less critical systems first
  Avoid interrupting any critical process phases
Notes: No patches available for windows NT, 98, ME
Windows 2000 supported only until 2010
Cisco and other released a patch for TCP support Sept 2009 (DOS prevention)

## Slide 17: Limited use of Host Anti-Virus
AV operations can cause significant system disruption at inopportune times
  3am is no better than any other time for a full disk scan on a system that operates 24x7x365
ICS vendors only beginning to support anti-virus
  Anti-virus is only as good as the signature set
  Signatures may require testing just like patches
AV may be losing ground in enterprise deployments
  impact on hosts, endpoint security not getting better
  virus writers have learned to test against dominant AV
application whitelisting can be a good alternative
  enumerate goodness rather than badness

## Slide 18: Poor Authentication and Authorization
Machine-to-machine comms involve no “user”
Many ICS have poor authentication mechanisms and very limited authorization mechanisms
Many protocols use cleartext passwords
Many ICS devices lack crypto support
Sometimes passwords left at vendor default
Device passwords are hard to manage appropriately
  Often one password is shared amongst all devices and all users and seldom if ever changed
  This is happening AGAIN in Smart Meter deployments!
Notes: Queensland
extreme example: password limited to 3 uppercase characters

## Slide 19: Poor Audit and Logging
Many ICS have poor or non-existent support for logging security-related actions
  Attempted or successful intrusions may go unnoticed
Where IDS logs are kept, they are often not reviewed
Various regulatory requirements are driving some change in this area
  NERC—North American Electric Reliability Corporation
  FERC—Federal Energy Regulatory Commission
  Sarbanes Oxley and PCAOB (Public Company Accounting Oversight Board)
  FISMA—Federal Information Security Management Act
Notes: SoX passed in response to scandals like Enron, relates to financial accounting, and the PCAOB auditing standard #2 states “IT Controls should be tested, including controls over relevant assertions related to all significant accounts and disclosures in the financial statements”

## Slide 20: Unmanned Field Sites
Many unmanned field sites
Many with dialup access
Some with high-speed connectivity to control center
Most with poor authentication and authorization
backdoor to the control center!

## Slide 21: Middle Protective Layers
Structure
  Door controls, window controls
  Ceiling penetration
  Ventilation ducts
  Elevator Penthouses
Environment
  Within defined perimeter, positive controls
Purpose
  Alert threat, segment protection zones

## Slide 22: Inner Protective Layers
Several layers
Structure
  Door controls, biometrics
  Signs, alarms, cctv
  Safes, vaults
Environment
  Authorized personnel only
Purpose
  Establish controlled areas and rooms

## Slide 23: Components
Accidental and environmental disasters
  Placing obstacles
  Idea is to confuse attacker, delay serious ones, and attempt to avoid the inevitable
Monitoring and notification systems
  Security mechanisms to monitor and detect potential harm or violations
  Alarms, security lighting, security guards or closed-circuit television cameras (CCTV)

## Slide 24: Components (cont.)
Recovery mechanisms
  To repel, catch or frustrate attackers when an attack is detected
  Intrusion handling

## Slide 25: Layers
Environment Design
  First layer of physical protection
  Consists of external design void off intruders
  May include objects like barbed wire, warning signs, fencing, metal barriers, and site lighting

## Slide 26: Layers (cont.)
Mechanical and electronic access control
  Prevents intruders or unauthorized users to direct access to physical components
  Includes gates, doors and locks

## Slide 27: Layers (cont.)

## Slide 28: Implementation
State the plan’s purpose
Define the areas, buildings, and other structures considered critical and establish priorities for their protection
Define and establish restrictions on access and movement of critical areas
  Categorize restrictions

## Slide 29: Layers (cont.)
Monitoring system
  Less of a preventative measure
  Used more for incident verification and analysis
  Most common mechanism is CCTVs

## Slide 30: Layers (cont.)
Intrusion Detection
  Monitors for attacks
  Less of a preventative measure
  More of an response mechanism
  Alarms/Notification

## Slide 31: Physical Security Briefs
Security site brief
  Security policies used for the framework of preventing the access to a physical setting
Security design brief
  Security policies used for the layout or design for a physical entity (may be coding, layout for servers, access control, etc)

## Slide 32: Zoning
Public Zone
  Public has access to this area of a facility and its surrounding
  Examples are facility grounds, elevator lobbies, etc
Reception Zone
  Zone which entail the transition from a public zone to a restricted-access area of control
  Typically means where the contact of visitors and a department is initiated

## Slide 33: Zones (cont.)
Operations Zone
  An area where access is limited to personnel who work at facility and to escorted visitors
  Production floors and open office areas
Security Zone
  An area to which access is limited to authorized personnel and to authorized and escorted visitors
  Area where secret information is processed/stored

## Slide 34: Layers (cont.)
High Security Zone
  An area where access is limited to authorized, appropriately screened personnel and authorized and properly escorted visitors
  A general example would be an area where high-value assets are handled by selected personnel

## Slide 35: Trust Me, I’m a doctor
Security often begins by developing a concept of trust that is within the risk appetite of the organization, then developing security measures based upon what are call Trust Zones.
  You’re likely familiar with this concept in browsers, but it’s used everywhere.
  Basically, less trust is required to access non-sensitive data. Maybe only a password. If the user wants access to a higher-level (more restricted) trust zone, they must identify themselves again. This could be the same factor as before, or with a second factor.
Some organizations have a culture of not automatically providing users access to areas/systems within common trust zones – these are called Zero-Trust Environments, and provide the best security at the expense of convenience.

## Slide 36: Zone restrictions require security
A security layer has to be established between zones in order to establish boundaries of the zone. Walls do most of this, but there must be ingress/egress.
A boundary is established by deterrents, like perimeter markers, security lights, warning signs, etc.

## Slide 37: Zone restrictions require security
A security layer is some manner of obstacle to prevent a subject from moving from one zone or another without being challenged.
  This could be a guard, but there are plenty of other options –locks, for example.
You can also maximize the efficiency of human resources by monitoring security layers to ensure they aren’t tampered with or intruded upon.
  A place without monitoring is a blind spot.

## Slide 38: Zone restrictions require security
Sometimes a zone is established between zones that establishes a buffer between zones – this is a DMZ.
As best practice, the most secure zone is contained in within increasingly restricted zones. This is called Depth of Security. A DMZ is absolutely necessary when this isn’t possible and a high security zone borders lower-tier zones.

## Slide 40: Passing Security Challenges
Identity Proofing – Ensuring credentials are issued only to authorized individuals.
User Recertification – Periodically ensuring user entitlements are appropriate and required.
Entitlement Review – Ensuring all requests for new access are examined and approved.

## Slide 41: Other Barrier Issues
Handling of trash or scrap
Fire:
  Temperature
  Smoke
Pollution:
  CO
  Radon
Flood
Earthquake

## Slide 42: Physical Restrictions
Air Gapping Data
    Limits access to various security levels
    Requires conscious effort to violate
    Protects against inadvertent transmission
Removable Media
    Removable Hard Drives
    Floppy Disks/CDs/ZIP Disks
Remote Storage of Data
    Physically separate storage facility
    Use of Storage Media or Stand Alone computers
    Updating of Stored Data and regular inventory

## Slide 43: Personnel Security Practices
Insider Threat the most serious
    Disgruntled employee
    Former employee
    Agent for hire
Personnel Training
    Critical Element
    Most often overlooked
Background checks
    Critical when access to information required
    Must be updated
    CIA/FBI embarrassed

## Slide 44: People
Disgruntled employee / former employee
Moonlighter
Marketing, sales representatives, etc.
Purchasing agents, buyers, subcontract administrators
Consultants
Vendor/Subcontractor
Clerical
Applicants, Visitors, Customers

## Slide 45: Activities or Events
Publications, public releases, etc.
Seminars, conventions or trade shows
Survey or questionnaire
Plant tours, “open house”, family visits
Governmental actions: certification, investigation
Construction and Repair

## Slide 46: Technical Security
Alarms
    Loud and Noisy
    Silent
    Integrated into barrier methods
Video/Audio
    Deterrent factor
    Difficult to archive
Bio-Metrics
    Identification
    Reliability questions

## Slide 47: Authentication
Mutli-Factor Authentication –
  Something you know
  Something you have
  Something you are
Co-Initiate System Factors –
  Temporal
  Geographic

## Slide 48: RFID Tech

## Slide 49: Biometrics – Characteristics
Notes: Section breaker slide with customer logo
Section heading – Arial Headings, 34, Bold
Sub head – Arial Headings, 18, normal
Used for a section heading. You may add a sub heading not exceeding one line also here
Section heading – Arial Headings, bold, 34 font size, should not exceed beyond 1 line
Sub Head – Arial Headings, normal, 18 font size, should not exceed beyond 1 line

## Slide 50: FRR, FAR and CER
Notes: Section breaker slide with customer logo
Section heading – Arial Headings, 34, Bold
Sub head – Arial Headings, 18, normal
Used for a section heading. You may add a sub heading not exceeding one line also here
Section heading – Arial Headings, bold, 34 font size, should not exceed beyond 1 line
Sub Head – Arial Headings, normal, 18 font size, should not exceed beyond 1 line

## Slide 55: Key Bitting

## Slide 56: If you see your principle using these keys…
C415A
C420A
C642A
1284X
2642
6642
1620
3910
CC1
FEO-K1
A126 linear
CH751
501CH
C346A
C390A
C413A
CC1